## Slide 1: MASTER’S COMMUNICATION SKILLS

## Slide 2: Communication with the shipping company
As the bureaucratic work is increasing, the amount of messages exchanged between a Vessel and the parent Company increases too.
Most Companies receive their messages from one source (email account) in order to be retrieved and read easily by all the different departments –if needed-, and they manage the “first to read” process by requesting the Vessel to tag the messages with key words such as the main Department to be concerned about the content, and/or abbreviations either on the “Subject” or on the beginning of the main messages’ body. Such abbreviations can be (list not exhaustive). “ENG” for Main Engine issues, “DG” for Diesel Generators issues, “DK” for Deck issues, “CARG” for cargo issues etc.

## Slide 3: Communication with shipping company (cont’d)
In the side picture we see such a request from a Company, as the messages that are related to monthly technical report forms be sent with a strict subject naming. Such strict naming format is usually required to messages that their content or attachments are automatically imported to external software for analysis of results or evaluation of technical aspects.

## Slide 4: Noon reports
SOLAS Chapter V regulation 28 §2 mandates that any Vessel above 500GRT engaged on international voyages greater than 48 hours (or “hrs” as you may see in much of the correspondence) are obliged to transmit by any means available (meaning email or telex or fax or MF/HF or , in extraordinary cases, voice) a report containing as a minimum,
A. The Ship’s position
B. The ship’s course and speed
C. The details of any occurrence that may affect the normal and safe operation and navigation of the Vessel.
It is customary such a report to be transmitted at Ship’s Noon Time, therefore it is called “Noon Position”.
The majority of the shipping Companies “embellish” the short SOLAS mandatory report with different requested data such as, information about engine performance, consumption, information about cargo temperature if it is critical, detailed weather conditions description etc.

## Slide 5: FORMAT OF NOON REPORTS
Noon reports (or Noonreps) are “closed format” messages. They follow a strict “proforma” format that mandates an exact wording and formatting of the message. Most of the times that formatting and wording is provided either directly on the SMS Manual (Safety Management System Manual) or on a Circular Letter.
Failure of following the proper specified format will result in improper evaluation of ship’s performance and/or disputes even with the charterers as mistakes p.e. in consumption, may create the conditions for financial claims.
In addition, we need to point that Noon Reports are always requested by charterers too.

## Slide 6: Exercise:
You are the 2nd Mate of “MT SUZIE Q” on her VOY 123.
Write a Noon Report addressed to the following Departments: Operations (OPS) – Technical (TECH) – Bunkers (BUNK).
“Subject” format must follow the following:
“SHIPS NAME<space>NOONRE<space>VOY NUMBER
First line of the msg body must be:
ATTN: [DEPARTMENT ABBREVIATED NAMES]
For the rest of the msg use the format on the previous slide.