## Slide 1
Designations
6 S 70 M E-B/C/GI7
Concept
C Camshaft controlled
E Electronically controlled
S Super long stroke
L Long stroke
K Short stroke
Number of cylinders
Design
Electronically controlled small bore engine
Compact engine
GI Gas Injection and compact
Engine programme
Diameter of piston in cm
Stroke/bore ratio
Mark version
ME Engine control system - Introduction to ME engine (Jan 2008)

## Slide 2
ME Engine
ME Engine control system - Introduction to ME engine (Jan 2008)

## Slide 3
New Components /
re-designed
Hydraulic Power Supply (HPS)
Hydraulic Cylinder Unit (HCU)
Engine Control System (ECS)
Starting air valves
Start and Reversing sequences Governor function
Auxiliary blowers
Electronically Profiled Injection (EPIC) Exhaust valve actuation
Cylinder lubrication (ACC)
Exhaust valve
Crankshaft position sensing system
Local Operation Panel (LOP)
ME Engine control system - Introduction to ME engine (Jan 2008)

## Slide 4
The ME Engine Hydraulic Oil Loop
EL. driven
hydraulic pumps
Engine driven
hydraulic pumps
Fuel 7 - 8 bar
Hydraulic
cylinder unit
ME lubricator
Servo oil
return to sump
Fine aut. Filter 6μ
Piston cooling
+ bearings
From Main lub oil pump, cooler and 50 μ filter
Valve block
Servo oil
Fuel oil pressure booster
Exhaust valve actuator
FIVA
Cyl. 1 CCU
Cyl. 2 CCU
Cyl. 3 CCU
Cyl. 4
CCU Cyl. 5 CCU
Cyl. 6
CCU
Approx 200 bar
ME Engine control system - Introduction to ME engine (Jan 2008)

## Slide 5
1) Distributor block
Components: FIVA
Accumulators Cylinder lubricator
Highpressure pipes
ME Engine control system - Hydraulic cylinder unit (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 6: Hydraulic Cylinder Units (HCU)
HCU’s mounted on a common base plate.
Double wall high pressure pipe
High pressure oil inlet from the HPS
ME Engine control system - Hydraulic cylinder unit (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 7
ME(-C) Hydraulic cylinder Unit (FIVA)
M05E-02E-2n0g0i4ne control s(2y5s0te0/mKN-BH) ydraulic cylinder unit (Jan 2008)
© MAN Diesel SE
2007/12/18
<5 >

## Slide 8: Accumulator
Nitrogen
Oil
Tool for dismantling of accumulator. The claws keeps the tool in place!
ME Engine control system - Hydraulic cylinder unit (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 9: Hydraulic Cylinder Unit - HCU
FIVA Proportional Valve (controlling fuel injection and exh. Valve operation
Distribution Block
Cylinder Lubricator
Fuel Oil Pressure Booster
Exhaust Valve Actuator
ME Engine control system - Introduction to ME engine (Jan 2008)

## Slide 10: Hydraulic Cylinder Units
ME Engine control system - Hydraulic cylinder unit (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 11
ME Fuel Oil Pressure Booster
MC versus ME
S50MC-C
S50ME-C
Fuel Plunger
Hydraulic actuator
Fuel oil inlet pressure 7 - 8 bar
Feed back Position sensor
Suction Valve
ME Engine control system - Introduction to ME engine (Jan 2008)

## Slide 12: Suction Valve, K98ME
ME Engine control system - Fuel system (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 13
Fuel Oil Injection
working principle
Phase 1
The pistons move to the bottom position.
The fuel inlet is open.
Hydraulic oil leaves the hydraulic oil chamber via the FIVA valve.
The accumulators are supplied by the Hydraulic Power Supply. The pressurised hydraulic oil is held back by the closed FIVA valve.
Unpressurised fuel oil Pressurised fuel oil Unpressurised hydraulic oil Pressurised hydraulic oil
FIVA
Valve
ME Engine control system - Fuel system (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 14
5.
The FIVA valve is activated upwards, closing the return flow and opening for the flow of pressurised hydraulic oil. The oil passes through the FIVA valve and fills the hydraulic chamber.
6.
The high pressure forces the pistons upwards.
The fuel oil inlet is closed.
The pressure on the fuel oil rises and exceeds the force of the spring in the cylinder’s fuel injection valve.
7.
8.
Unpressurised fuel oil Pressurised fuel oil Unpressurised hydraulic oil Pressurised hydraulic oil
FIVA
Valve
working principle
Phase 2
Fuel injection
ME Engine control system - Fuel system (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 15: Exhaust valve actuator
The FIVA valve which drives the actuator on the exhaust side has two positions, open or shut.
When it is opened with a binary signal from the engine control system, the hydraulic oil is forced in and pushes the pistons upwards,thus opening the engine’s exhaust valve via the hydraulic push rod.
The pressure is permanently maintained until the FIVA valve is activated to block
the pressure when the required exhaust phase is completed.
The exhaust valve is returned to its closed position by the force from the air spring.
Unpressurised hydraulic oil Pressurised hydraulic oil
FIVA
Actuator
working principle
ME Engine control system - Exhaust system (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 16: MC versus ME
FIVA on-off valve
Exhaust valve spindle
High pressure hydraulic oil – inlet
Membrane accumulator
Hydraulic push rod
Exhaust valve Actuator
Exhaust valve system
ME Engine control system - Introduction to ME engine (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 17: Exhaust valve
S50MC-C
S50ME-C
Hydraulic damper for fixed valve stroke introduced
Air spring size for closing the exhaust valve reduced
New valve spindle design introduced
MC versus ME
ME Engine control system - Exhaust system (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 18
ME Tacho-system
M0E4-E11n-2g20in0e3 control2s5y0s0/tKeNNmB - ME Concept (Jan 2008)
© MAN Diesel SE
2007/12/18
< 28 >

## Slide 19: Tacho system
Angle encoders
TSA-A
TSA-B
4001-A
4002-A
4003-A
4004-A
4001-B
4002-B
4003-B
4004-B
ECU’s
+ CCU’s
90 deg ATDC
0 deg
(TDC 1)
45 deg ATDC
Angle encoder A
Angle encoder B
ME Engine control system - ME Concept (Jan 2008)
© MAN Diesel SE
2007/12/18
< 29 >

## Slide 20
ME Tacho-system
M04E-1E1-n2g000in3e contro2l5s0y0s/KteNmB - ME Concept (Jan 2008)
© MAN Diesel SE
2007/12/18
< 31 >

## Slide 21
Tacho System Amplifier boxes, TSA
ME Engine control system - ME Concept (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 22
Tacho system, semicircular ring
ME Engine control system - ME Concept (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 23: ME Tacho-system
Trigger rings + sensors (option)
2 redundant set of sensors.
Each set measure engine speed and crankshaft position for synchronization of the control events.
Each set consist of four sensors. Two quadrature sensors measure on a trigger ring with 360 tooth and two marker sensors measures on a semicircular ring.
Triiggersegment with a siine-curved tooth- profile The total trigger ring is built by 8 equal segments.
M2E20E0/nOgZiSSn//e03c0o2n12trol system - ME Concept (Jan 2008)
© MAN Diesel SE
2007/12/18
< 36 >

## Slide 24
Maintenance Network Status
ME Engine control system - Engine operation (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 25
Alarms: Event Log
ME Engine control system - Engine operation (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 26: ME Engine Control System
Bridge
Engine Control Room
Engine Room/On Engine
Main Operating Panel
PC
Control Room Panel
BACK-UP FOR MOP
Bridge Panel
ACU
CCU
ECU A
EICU A EICU B
Engine Interface Control Units A and B
Auxiliariy Control Units 1, 2 and 3
ECU B
Cylinder Control Units 1 per cylinder
Engine Control Units A and B
Local Operation Panel
Control Network
Multi-Purpose Controller
ME Engine control system - Introduction to ME engine (Jan 2008)

## Slide 27: Multi Purpose Controller
MPC
Amplifier for FIVA (CCU’s) and Hydraulic pumps (ACU’s)
’IP 66’ cabinet
Multi Purpose Controller
ME Engine control system - ME Concept (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 28
MPC’s Nordic Brasilia – 6S70ME-C
ME Engine control system - ME Concept (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 29: Start block
Engine Control Unit, ECU
Check list of conditions which must be in order before engine start
One list for ’Standby’ and another list for ’FWE’ (Finished With Engine),
ME Engine control system - ME Concept (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 30
ME Starting Air System
ME-C design
Pilot air inlet
Starting valves
NC-valves
Blow-off
Connection for
ECS
MC-C design
Starting valves
Starting air distributor
ME Engine control system - ME Concept (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 31: Starting air-
and pilot air valve
Starting air valve
Pilot air valve
ME Engine control system - ME Concept (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 32: Electrical driven start-up pumps
ME Engine control system - Hydraulic Power Supply (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 33
Swash plate principle
Flow
Stroke
α
The stroke is given by the α angle
ME Engine control system - Hydraulic Power Supply (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 34
Axial piston pump –
Rotating parts
Suction side
Pressure side
Pistons
ME Engine control system - Hydraulic Power Supply (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 35: Axial piston pump
Pump sizes:
125 ccm/rev - 3 pumps
180 ccm/rev - 3 pumps
250 ccm/rev - 3 pumps
355 ccm/rev - 3 pumps
500 ccm/rev - 3 to 5 pumps
ME Engine control system - Hydraulic Power Supply (Jan 2008)
© MAN Diesel SE
2007/12/18
< >

## Slide 36
ME – Engine, Pump Drive and Moment Compensator
ML/E73E89n8g-1in.0e/0c3o03ntro(l2s60y0s/tReØmL)- Hydraulic Power Supply (Jan 2008)
© MAN Diesel SE
2007/12/18
< 21 >